STM32 Computer
# Introduction
STM32MP15XXAC
## Formulas
### Critical length
l_crit = {300t_{r/t}} over {4 sqrt{ %varepsilon } }
# Impedance
## Stack
The stack is JLC04161H-1080 with finished thickness 1.52 mm.
Layer	Material	Thickness (mil)	Thickness (mm)
L1	Outer Copper Weight 1oz	1.38	0.0350
Prepreg	1080 RC67% 3.3mil, ε = 3.91	3.01	0.0764
L2	Inner Cooper Weight 0.5oz	0.60	0.0152
Core	1.3mm H/HOZ with copper, ε = 3.91	49.80	1.2650
L3	Inner Cooper Weight 0.5oz	0.60	0.0152
Prepreg	1080 RC67% 3.3mil, ε = 3.91	3.01	0.0764
L4	Outer Copper Weight 1oz	1.38	0.0350

## PMIC

## HDMI
Connection from	Pin	Connection to	Pin	Signal type	Other
STM32MP15	AC4	SII9022ACNU	CSCL	Clock	Pull-up
STM32MP15	Y4	SII9022ACNU	CSDA	Data	Pull-up
Decoupling	N/A	SII9022ACNU	IOVCC	Power	3.3V
STM32MP15	D3	SII9022ACNU	D23	Data	N/A
Decoupling + resistor	N/A	SII9022ACNU	CVCC12	Power	1.2V
STM32MP15	B2	SII9022ACNU	D22	Data	N/A
STM32MP15	AB5	SII9022ACNU	D21	Data	N/A
STM32MP15	C2	SII9022ACNU	D20	Data	N/A
STM32MP15	C5	SII9022ACNU	D19	Data	N/A
STM32MP15	D5	SII9022ACNU	D18	Data	N/A
STM32MP15	AA3	SII9022ACNU	D17	Data	N/A
STM32MP15	AB4	SII9022ACNU	D16	Data	N/A
STM32MP15	E2	SII9022ACNU	D15	Data	N/A
STM32MP15	E3	SII9022ACNU	D14	Data	N/A
STM32MP15	C1	SII9022ACNU	D13	Data	N/A
STM32MP15	B1	SII9022ACNU	D12	Data	N/A
STM32MP15	C3	SII9022ACNU	D11	Data	N/A
STM32MP15	D1	SII9022ACNU	D10	Data	N/A
STM32MP15	C10	SII9022ACNU	D9	Data	N/A
STM32MP15	AC14	SII9022ACNU	IDCK	Clock	N/A
STM32MP15	AA7	SII9022ACNU	D8	Data	N/A
STM32MP15	K3	SII9022ACNU	D7	Data	N/A
STM32MP15	K3	SII9022ACNU	D6	Data	N/A
STM32MP15	U2	SII9022ACNU	D5	Data	N/A
STM32MP15	E4	SII9022ACNU	D4	Data	N/A
STM32MP15	B5	SII9022ACNU	D3	Data	N/A
STM32MP15	AB11	SII9022ACNU	D2	Data	N/A
STM32MP15	K4	SII9022ACNU	D1	Data	N/A
STM32MP15	K1	SII9022ACNU	D0	Data	N/A
STM32MP15	Y12	SII9022ACNU	DE	Enable	N/A
STM32MP15	T1	SII9022ACNU	HSYNC	Data	N/A
STM32MP15	H4	SII9022ACNU	VSYNC	Data	N/A
STM32MP15	E1	SII9022ACNU	SD0	Data	N/A
STM32MP15	AC5	SII9022ACNU	WS	Data	N/A
STM32MP15	A8	SII9022ACNU	CK	Clock	N/A (Audio?)
HDMI Connector	16	SII9022ACNU	DSDA	Data	ESD protection
HDMI Connector	15	SII9022ACNU	DSCL	Clock	ESD protection
STM32MP15	Y14	SII9022ACNU	CEC_D	Data	N/A
STM32MP15	AC13	SII9022ACNU	RESET#	Reset	N/A
STM32MP15	W1	SII9022ACNU	INT	Interrupt	N/A
HDMI Connector	19	SII9022ACNU	HPD	Detection	Pull-up + ESD
Resistor 5.1K	N/A	SII9022ACNU	EXT_SWING	Adjustment	Pull-down
HDMI Connector	12	SII9022ACNU	TXC -	Data -	Differential
HDMI Connector	10	SII9022ACNU	TXC +	Data +	Differential
HDMI Connector	9	SII9022ACNU	TX0 -	Data -	Differential
HDMI Connector	7	SII9022ACNU	TX0 +	Data +	Differential
HDMI Connector	6	SII9022ACNU	TX1 -	Data -	Differential
HDMI Connector	4	SII9022ACNU	TX1 +	Data +	Differential
HDMI Connector	3	SII9022ACNU	TX2 -	Data -	Differential
HDMI Connector	1	SII9022ACNU	TX2 +	Data +	Differential
HDMI Connector	13	SII9022ACNU	CEC_A	Indicator	ESD

## USB Host
This is USB host, 4x A-ports.
Connection from	Pin	Connection to	Pin	Signal type	Other
DM_T	T2	USB2514B	USBDM_DN1	Data -	Passing ECMF02-2AMX6
DP_T	T3	USB2514B	USBDP_DN1	Data +	Passing ECMF02-2AMX6
DM_B	B2	USB2514B	USBDM_DN2	Data -	Passing ECMF02-2AMX6
DP_B	B3	USB2514B	USBDP_DN2	Data +	Passing ECMF02-2AMX6
Decopuling	N/A	USB2514B	VDDA33	Power	3.3V
DM_T	T2	USB2514B	USBDM_DN3	Data -	Passing ECMF02-2AMX6
DP_T	T3	USB2514B	USBDP_DN3	Data +	Passing ECMF02-2AMX6
DM_B	B2	USB2514B	USBDM_DN4	Data -	Passing ECMF02-2AMX6
DP_B	B3	USB2514B	USBDP_DN4	Data +	Passing ECMF02-2AMX6
GND	N/A	USB2514B	TEST	NC	N/A
STMPS2252MTR	3	USB2514B	PRTPRW1	Enable signal	N/A
STMPS2252MTR	8	USB2514B	OCS_N1	Over current signal	N/A
100nF	N/A	USB2514B	CRFILT	Filter capacitor	N/A
Decopuling	N/A	USB2514B	VDD33	Power	3.3V
STMPS2252MTR	4	USB2514B	PRTPRW2	Enable signal	N/A
STMPS2252MTR	5	USB2514B	OCS_N2	Over current signal	N/A
STMPS2252MTR	3	USB2514B	PRTPRW3	Enable signal	N/A
STMPS2252MTR	8	USB2514B	OCS_N3	Over current signal	N/A
STMPS2252MTR	4	USB2514B	PRTPRW4	Enable signal	N/A
STMPS2252MTR	5	USB2514B	OCS_N4	Over current signal	N/A
STM32MP15	AA19	USB2514B	NON_REM[1]	Data	Pull-up/down
STM32MP15	Y18	USB2514B	CFG_SEL[0]	Clock	Pull-up/down
N/A	N/A	USB2514B	CFG_SEL[1]	Config	Pull-up/down
N/A	N/A	USB2514B	RESET_N	Reset	Pull-up 10K
N/A	N/A	USB2514B	VBUS_DET	Config	Pull-up 10K
LED	N/A	USB2514B	NON_REM[0]	Config	Pull-down 10K
STM32MP15	AB17	USB2514B	USBDM_DP	Data -	Differential
STM32MP15	AC17	USB2514B	USBDP_DP	Data +	Differential
NX2016SA	1	USB2514B	XTALOUT	Crystal 24 MHz	0R resistor + decoplings
NX2016SA	3	USB2514B	XTALIN	Crystal 24 MHz	0R resistor + decoplings
100nF	N/A	USB2514B	PLLFILT	Filter capacitor	N/A
Resistor	N/A	USB2514B	RBIAS	Config	Pull-down 12K

RX/TX rise time: t_{r/t} = 0.75 ns.
Name	Trace length (mm)	Vias	Impedance resistor (ohm)	Trace width (mm)	Impedance (ohm)	Route	Spacing (mm)	Critical length (mm)
USBDM_DN1	12.401	0	N/A	0.13	90	Data -	0.24	N/A
USBDP_DN1	12.503	0	N/A	0.13	90	Data +	0.24	N/A
USBDM_DN2	15.88	0	N/A	0.13	90	Data -	0.24	N/A
USBDP_DN2	15.88	0	N/A	0.13	90	Data +	0.24	N/A
USBDM_DN3	15.308	0	N/A	0.13	90	Data -	0.24	N/A
USBDP_DN3	15.338	0	N/A	0.13	90	Data +	0.24	N/A
USBDM_DN4	20.578	0	N/A	0.13	90	Data -	0.24	N/A
USBDP_DN4	20.578	0	N/A	0.13	90	Data +	0.24	N/A
USBDM_UP	32.487	0	N/A	0.13	90	Data -	0.24	N/A
USBDP_UP	32.434	0	N/A	0.13	90	Data +	0.24	N/A

## Reduced Gigabit Media-Independent Interface (RGMII)
The Reduced Gigabit Media-Independent Interface (RGMII) is using the twisted pair cable 1000BASE-T. The connections between the processor STM32MP15XXAC and Ethernet PHY Realtek RTL8211F-CG are:
Connection from	Pin	Connection to	Pin	Signal type	Other
J0G-0001NL	11	RTL8211F-CG	MPIP0	Data +	Differential
J0G-0001NL	10	RTL8211F-CG	MPIN0	Data -	Differential
Decopuling + ferrite	N/A	RTL8211F-CG	AVDD10	Power	1.05V
J0G-0001NL	4	RTL8211F-CG	MPIP1	Data +	Differential
J0G-0001NL	5	RTL8211F-CG	MPIN1	Data -	Differential
J0G-0001NL	3	RTL8211F-CG	MPIP2	Data +	Differential
J0G-0001NL	2	RTL8211F-CG	MPIN2	Data -	Differential
J0G-0001NL	8	RTL8211F-CG	MPIP3	Data +	Differential
J0G-0001NL	9	RTL8211F-CG	MPIN3	Data -	Differential
Decopuling + ferrite	N/A	RTL8211F-CG	AVDD33	Power	3.3V
Pull-up 10K	N/A	RTL8211F-CG	PHYRSTB	Hardware Reset	3.3V
STM32MP15	AA6	RTL8211F-CG	MDC	Clock	Pull-up 1.5K
STM32MP15	AC3	RTL8211F-CG	MDIO	Data	Pull-up 1.5K
STM32MP15	Y1	RTL8211F-CG	TXD3	Data	N/A
STM32MP15	Y2	RTL8211F-CG	TXD2	Data	N/A
STM32MP15	AA1	RTL8211F-CG	TXD1	Data	N/A
STM32MP15	AA2	RTL8211F-CG	TXD0	Data	N/A
STM32MP15	AB1	RTL8211F-CG	TXCTL	Control	N/A
STM32MP15	AB2	RTL8211F-CG	TXC	Clock	N/A
Decopuling + ferrite	N/A	RTL8211F-CG	DVDD10	Power	1.05V
STM32MP15	W4	RTL8211F-CG	RXD3	Data	Impedance resistor + pull-up 4.7K
STM32MP15	AB6	RTL8211F-CG	RXD2	Data	Impedance resistor + pull-down 4.7K
STM32MP15	AB7	RTL8211F-CG	RXD1	Data	Impedance resistor + pull-up 4.7K
STM32MP15	AC7	RTL8211F-CG	RXD0	Data	Impedance resistor + pull-up 4.7K
STM32MP15	AB8	RTL8211F-CG	RXCTL	Control	Zero ohm resistor + pull-down 4.7K
STM32MP15	AA4	RTL8211F-CG	RXC	Clock	Zero ohm resistor + pull-down 4.7K
Decopuling + ferrite	N/A	RTL8211F-CG	DVDD_RG	Power	N/A
Decopuling + ferrite	N/A	RTL8211F-CG	DVDD	Power	N/A
2.2µH or 4.7µH inductor	N/A	RTL8211F-CG	REG_OUT	Regulator	1.05V
STM32MP15	AC8 (ej int)	RTL8211F-CG	INTB	External interupt	Pull-up 1.5K
LED Green	N/A	RTL8211F-CG	CFG_EXT	Config	Pull-up 4.7K
LED Yellow	N/A	RTL8211F-CG	CFG_LD0	Config	Pull-down 4.7K
LED Green	N/A	RTL8211F-CG	CFG_LD1	Config	Pull-down 4.7K
STM32MP15	Y6	RTL8211F-CG	CLKOUT	Clock 125MHz	Impedance resistor
NX3225GA	1	RTL8211F-CG	XTAL_IN	Crystal 25MHz	0R resistor + decoplings
NX3225GA	3	RTL8211F-CG	XTAL_OUT	Clock 25MHz	0R resistor + decoplings
2.49K resistor	N/A	RTL8211F-CG	RSET	Regulator reference	2.49K pull-down

Impedance
RX/TX rise time: t_{r/t} = 0.75 ns.
Name	Trace length (mm)	Vias	Impedance resistor (ohm)	Trace width (mm)	Impedance (ohm)	Route	Spacing (mm)	Critical length (mm)
ETH_GTX_CLK	21.011	0	N/A	0.11	50	Single / Non coplanar	N/A	28.447
ETH_TX_EN	20.962 (17.762)	2	N/A	0.11	50	Single / Non coplanar	N/A	28.447
ETH_TXD0	20.936 (17.736)	2	N/A	0.11	50	Single / Non coplanar	N/A	28.447
ETH_TXD1	20.947 (17.747)	2	N/A	0.11	50	Single / Non coplanar	N/A	28.447
ETH_TXD2	20.906 (17.706)	2	N/A	0.11	50	Single / Non coplanar	N/A	28.447
ETH_TXD3	20.987 (17.787)	2	N/A	0.11	50	Single / Non coplanar	N/A	28.447
ETH_RX_CLK	29.286 (24.486)	3	0	0.11	50	Single / Non coplanar	N/A	28.447
ETH_RX_DV	29.280 (24.480)	3	0	0.11	50	Single / Non coplanar	N/A	28.447
ETH_RXD0	29.121 (24.321)	3	22	0.11	50	Single / Non coplanar	N/A	28.447
ETH_RXD1	29.110 (24.310)	3	22	0.11	50	Single / Non coplanar	N/A	28.447
ETH_RXD2	29.158 (24.358)	3	22	0.11	50	Single / Non coplanar	N/A	28.447
ETH_RXD3	29.127 (24.327)	3	22	0.11	50	Single / Non coplanar	N/A	28.447
RJ45_D4	P 26.841 / N 28.545	0	N/A	0.103	100	Differential / Non coplanar	0.24
RJ45_D3	P 26.467 / N 27.035	0	N/A	0.103	100	Differential / Non coplanar	0.24
RJ45_D2	P 28.046 / N 29.751	0	N/A	0.103	100	Differential / Non coplanar	0.24
RJ45_D1	P 21.775 / N 22.343	0	N/A	0.103	100	Differential / Non coplanar	0.24